## Slide 1
PA Man:
Prefetch-Aware Cache Management for High Performance Caching
Carole-Jean Wu¶, Aamer Jaleel*, Margaret Martonosi¶, Simon Steely Jr.*, Joel Emer*§
Princeton University¶ Intel VSSAD* MIT§
December 7, 2011
International Symposium on Microarchitecture
Notes: <number>

## Slide 2
Memory Latency is Performance Bottleneck
Many commonly studied memory optimization techniques
Our work studies two:
Prefetching
  For our workloads, prefetching alone improves performance by an avg. of 35%
Intelligent Last-Level Cache (LLC) Management
2
Chart: IPC Performance Normalized to LRU
| No Prefetching | All | 1 | 1.036740012 | 1.040497033 | 1.064401995
LRU | 1 | nan | nan | nan | nan | nan
DRRIP | 1.0367 | nan | nan | nan | nan | nan
SDBP | 1.0405 | nan | nan | nan | nan | nan
SHiP-PC | 1.0644 | nan | nan | nan | nan | nan
[ISCA `10]
[MICRO `10]
[MICRO `11]
LLC management alone
Notes: This work is the first that investigates
<number>

## Slide 3
L2 Prefetcher: LLC Misses
CPU0
L1I
LLC
L2
CPU1
L2
CPU2
L2
CPU3
L2
L1D
L1I
L1D
L1I
L1D
L1I
L1D
PF
PF
PF
PF
Miss
Miss
. . .
Notes: When prefetching a specific address the first time, ….
2 types of requests: prefetch & demand requests going to the LLC.
<number>

## Slide 4
L2 Prefetcher: LLC Hits
CPU0
L1I
LLC
L2
CPU1
L2
CPU2
L2
CPU3
L2
L1D
L1I
L1D
L1I
L1D
L1I
L1D
PF
PF
PF
PF
Miss
Hit
. . .
Notes: <number>

## Slide 5
Prefetching Intelligent LLC Management
Notes: Let’s see what happens when applying the 2 commonly used memory latency optimization techniques together,
<number>

## Slide 6
Observation 1: For Not-Easily-Prefetchable Applications…
Chart: IPC Performance with Prefetching (Normalized to LRU without Prefetching)
LRU | 1.0942 | 0.88241 | 0.93703 | 1.606 | 0.79494 | 0.69716 | 3.6748 | 4.0297 | 2.5594
DRRIP | 1.1026 | 0.96832 | 1.0407 | 1.6102 | 0.94712 | 0.93462 | 3.6482 | 4 | 2.6659
SDBP | 1.0669 | 1.0021 | 1.1034 | 1.6099 | 1.04 | 0.8628 | 3.6742 | 4.0342 | 2.8512
SHiP-PC | 1.1658 | 1.1533 | 1.057 | 1.6269 | 1.0578 | 0.8526 | 3.412 | 3.8419 | 2.8734
Observation 1: Cache pollution causes unexpected performance degradation despite intelligent LLC Management
Notes: <number>

## Slide 7
Chart: IPC Performance Normalized to LRU
| Prefetching | SPEC CPU2006
LRU | 1 | nan
DRRIP | 1.0017 | nan
SDBP | 1.0108 | nan
SHiP-PC | 1.03 | nan
Chart: IPC Performance Normalized to LRU
| No Prefetching | SPEC CPU2006
LRU | 1 | nan
DRRIP | 1.0295 | nan
SDBP | 1.0352 | nan
SHiP-PC | 1.0654 | nan
Observation 2: For Prefetching-Friendly Applications
6.5%+
3.0%+
4
Observation 2: Prefetched data in LLC diminishes the performance gains from intelligent LLC management.
SPEC CPU2006
No Prefetching
SPEC CPU2006
Prefetching
Notes: Is halved.
<number>

## Slide 8
Design Dimensions for Prefetcher/Cache Management
✔
✗
✔
✗
Moderate
(pf. bit/line)
Some
(new hw.)
✔
✗
Software
Synergistic management for prefetchers and intelligent LLC management
Notes: <number>

## Slide 9
PACMan: Prefetch-Aware Cache Management
Research Question 2:
For applications already benefiting from prefetching,
can PACMan improve performance even more?
Research Question 1:
For applications suffering from prefetcher cache pollution,
can PACMan minimize such interference?
Notes: The two important observations for the interaction between intelligent LLC management and hardware prefetching
lead to our work for prefetch-aware cache management (called PACMan).
<number>

## Slide 10
Talk Outline
Motivation
PACMan: Prefetch-Aware Cache Management
PACMan-M
PACMan-H
PACMan-HM
PACMan-Dyn
Performance Evaluation
Conclusion
Notes: <number>

## Slide 11
Opportunities for a More Intelligent Cache Management Policy
A cache line’s state is naturally updated when
Inserting an incoming cache line @ cache miss
Updating a cache line’s state @ cache hit
11
14
Cache line is
re-referenced
Cache line is
inserted
Cache line is
re-referenced
Cache line is
re-referenced
Cache line is
evicted
0
Imme-
diate
1
Inter-
mediate
2
far
3
distant
No victim is
found
No victim is
found
No victim is
found
Re-Reference Interval Prediction (RRIP) ISCA `10
PACMan treats demand and prefetch requests differently at cache insertion and hit promotion
Notes: <number>

## Slide 12
PACMan-M: Treat Prefetch Requests Differently at Cache Misses
Reducing prefetcher cache pollution at cache line insertion
14
0
Imme-
diate
1
Inter-
mediate
2
far
3
distant
Cache line is
re-referenced
Cache line is
inserted
Cache line is
re-referenced
Cache line is
re-referenced
Cache line is
evicted
Prefetch
Demand
Notes: <number>

## Slide 13
PACMan-H: Treat Prefetch Requests Differently at Cache Hits
Retaining more “valuable” cache lines at cache hit promotion
16
0
Imme-
diate
1
Inter-
mediate
2
far
3
distant
Cache line is
re-referenced
Cache line is
inserted
Cache line is
re-referenced
Cache line is
re-referenced
Cache line is
evicted
Prefetch Hit
Demand Hit
Prefetch Hit
Demand Hit
Prefetch Hit
Demand Hit
Notes: Similar to PACMan-M, PACMan-H deprioritizes prefetch requests over demand requests that hit in the cache.
Cache lines referenced by demand requests are “more valuable”  PACMan-H retains these lines
<number>

## Slide 14
PACMan-HM = PAMan-H + PACMan-M
0
Imme-
diate
1
Inter-
mediate
2
far
3
distant
Cache line is
re-referenced
Cache line is
inserted
Cache line is
re-referenced
Cache line is
re-referenced
Cache line is
evicted
Prefetch Miss
Demand Miss
Prefetch Hit
Demand Hit
Prefetch Hit
Demand Hit
Prefetch Hit
Demand Hit

## Slide 15
SDM
Baseline + PACMan-M
PACMan-Dyn dynamically chooses between static PACMan policies
Follower Sets
SDM
Baseline + PACMan-HM
index
Cnt policy1
Cnt policy3
Cnt policy2
MIN
Policy Selection
.
.
.
.
SDM
Baseline + PACMan-H
Set Dueling
19

## Slide 16
Evaluation Methodology
CMP$im simulation framework
4-way OOO processor
128-entry ROB
3-level cache hierarchy
  L1 inst. and data caches: 32KB, 4-way, private, 1-cycle
  L2 unified cache: 256KB, 8-way, private, 10-cycle
  L3 last-level cache: 1MB per core, 16-way, shared, 30-cycle
Main memory: 32 outstanding requests, 200-cycle
Streamer prefetcher – 16 stream detectors
DRRIP-based LLC: 2-bit RRIP counter
Notes: <number>

## Slide 17
PACMan-HM Outperforms PACMan-H and PACMan-M
Chart: Performance Normalized to LRU in the Presence of Prefetching
DRRIP | 1.0076 | 1.0974 | 1.1106 | 1.0027 | 1.1914 | 1.3406 | 0.99277 | 0.99263 | 1.0416 | 1.0345 | 1.1157 | 1.0017 | 1.0434
PACMan-M | 1.0079 | 1.3049 | 1.3742 | 1.0091 | 1.4892 | 1.5246 | 0.92489 | 0.92142 | 1.2411 | 1.1281 | 1.3038 | 1.023 | 1.1297
PACMan-H | 1.0435 | 1.173 | 1.1206 | 1.0019 | 1.2054 | 1.5217 | 0.98457 | 0.99318 | 1.1758 | 1.0619 | 1.1784 | 1.0218 | 1.0756
PACMan-HM | 1.0206 | 1.3051 | 1.4878 | 1.0082 | 1.5834 | 1.6653 | 0.92466 | 0.92016 | 1.3004 | 1.1532 | 1.3609 | 1.0314 | 1.1547
While PACMan policies improve performance overall,
static PACMan policies can hurt some applications i.e. bwaves and gemsFDTD
Notes: <number>

## Slide 18
Chart: Performance Normalized to LRU in the Presence of Prefetching
DRRIP | 1.0076 | 1.0974 | 1.1106 | 1.0027 | 1.1914 | 1.3406 | 0.99277 | 0.99263 | 1.0416 | 1.0345 | 1.1157 | 1.0017 | 1.0434
PACMan-M | 1.0079 | 1.3049 | 1.3742 | 1.0091 | 1.4892 | 1.5246 | 0.92489 | 0.92142 | 1.2411 | 1.1281 | 1.3038 | 1.023 | 1.1297
PACMan-H | 1.0435 | 1.173 | 1.1206 | 1.0019 | 1.2054 | 1.5217 | 0.98457 | 0.99318 | 1.1758 | 1.0619 | 1.1784 | 1.0218 | 1.0756
PACMan-HM | 1.0206 | 1.3051 | 1.4878 | 1.0082 | 1.5834 | 1.6653 | 0.92466 | 0.92016 | 1.3004 | 1.1532 | 1.3609 | 1.0314 | 1.1547
PACMan-DYN | 1.0628 | 1.3012 | 1.4527 | 1.0081 | 1.5665 | 1.6423 | 0.95486 | 0.98821 | 1.363 | 1.1548 | 1.3515 | 1.0631 | 1.1648
PACMan-Dyn: Better and More Predictable Performance Gains
PACMan-Dyn performs the best (overall) while providing more consistent performance gains.
Notes: <number>

## Slide 19
PACMan: Prefetch-Aware Cache Management
Research Question 2:
For applications already benefiting from prefetching,
can PACMan improve performance even more?
Research Question 1:
For applications suffering from prefetcher cache pollution,
can PACMan minimize such interference?
Notes: <number>

## Slide 20
PACMan Combines Benefits of Intelligent LLC Management and Prefetching
Chart: IPC Performance Normalized to Baseline LRU without Prefetching
LRU | 1.0887 | 0.95717 | 2.2597 | 1.3304
DRRIP | 1.1263 | 1.0491 | 2.2636 | 1.3881
PACMan-HM | 1.2554 | 1.2391 | 2.3306 | 1.5362
PACMan-DYN | 1.2573 | 1.2319 | 2.4023 | 1.5496
22% better
15% better
Prefetch-Induced
LLC Interference
Prefetching
Friendly
Notes: <number>

## Slide 21
Other Topics in the Paper
PACMan-Dyn-Local/Global for multiprog. workloads
An avg. of 21.0% perf. improvement
PACMan cache size sensitivity
PACMan for inclusive, non-inclusive, and exclusive cache hierarchies
PACMan’s impact on memory bandwidth
Notes: <number>

## Slide 22
PACMan Conclusion
First synergistic approach for prefetching and intelligent LLC management
Prefetch-aware cache insertion and update
~21% performance improvement
Minimal hardware storage overhead
PACMan’s Fine-Grained Prefetcher Control
Reduces performance variability from prefetching
Notes: <number>

## Slide 23
PA Man:
Prefetch-Aware Cache Management for High Performance Caching
Carole-Jean Wu¶, Aamer Jaleel*, Margaret Martonosi¶, Simon Steely Jr.*, Joel Emer*§
Princeton University¶ Intel VSSAD* MIT§
December 7, 2011
International Symposium on Microarchitecture
Notes: <number>