## Slide 1
Chart: Reduction rate of L2 cache miss rate
| Cholesky | FMM | LU | Ocean | Radix | Raytrace
PB-GS | 0.31327 | 0.023572 | -0.10473 | 0.39747 | 0.59897 | 0.27975
PB-LS | 0.64295 | 0.10762 | 0.27215 | 0.62403 | 0.65038 | 0.32885
Chart: Speedup
| Cholesky | FMM | LU | Ocean | Radix | Raytrace
BASE | 1 | 1 | 1 | 1 | 1 | 1
PB-GS | 1.33 | 0.93485 | 0.94158 | 0.80886 | 0.79374 | 1.0421
PB-LS | 1.4666 | 0.9635 | 0.982 | 1.2558 | 0.82561 | 1.0602
Chart: Number of Cores
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
L2-1MB | 1 | 1.5011 | 1.677 | 1.8482 | 1.928 | 1.9692 | 2.0132 | 2.1054
L2-Perfect | 1.3352 | 2.2313 | 2.623 | 3.1206 | 3.2971 | 3.4949 | 3.6098 | 3.8415
Our approach!
6.9%
Perfect L2 cache
(hit rate 100% )
1MB L2 cache
Cholesky
47% speedup
BASE: All cores are used to execute the application-threads.
PB-GS(PB-LS) : The model supporting performance balancing, and
executes global(local) stride prefetch as helper threads.
shared bus
core1
L1D$
L1I$
MSB
core0
L1D$
L1I$
MSB
coreN
L1D$
L1I$
MSB
execute an application thread
execute a helper thread
…
computing cores
helper cores
…
compute intensive
memory intensive
L2 shared cache
main memory
on-chip
off-chip
The number of helper-cores
Relative execution cycles
Conventional
Proposal
Reduction rate of
L2 cache miss rate
Speed-Down
Speed-Up!
Performance analysis of Cholesky ( =0.73, =0.45)
If the effect of the software prefetching is larger than
the negative impact of the TLP throttling,
we can improve the CMP performance.
Performance Balancing: An Adaptive Helper-Thread Execution for Many-Core Era
Authors: Kenichi Imazato, Naoto Fukumoto, Koji Inoue, Kazuaki Murakami
(Kyushu University)
Conventional approach： All cores execute a parallel program
  Performance improvement is very small even if we increase the number of cores from 6 to 8.
Our approach： Core management considering the balance of processor-memory performance (Performance Balancing).
  Some cores are used to improve the memory performance
    Execute helper-threads for prefetching
Goal： High-Performance parallel processing on a chip multiprocessor
For prefetching, helper cores need the information for cache misses caused by computing cores.
Miss Status Buffer (MSB): Records the information for cache misses caused by computing cores.
  Each entry consists of a core-ID, a PC value, and an associated miss address.
  Each core has an MSB. → Helper-threads can be executed on any core.
The cache-miss information can be obtained by snooping the coherence traffic.
By referring MSB, helper-thread emulates hardware prefetchers.
Helper cores work for computing cores.
By exploiting profile information, compiler can statically optimize the number of helper cores.
By monitoring the processor and memory performance, the OS determines the number of helper-cores and the type of prefetchers.
  If memory performance is quite low, OS increases the number of helper-cores.
Introduce MSB
1. Concept
2. Architectural Support
3. Analysis
4. Preliminary Evaluation
The number of cores on a chip
The fraction of operations that can be parallelized
The number of helper cores
Reduction rate of L2 cache misses achieved by helper cores
The fraction of main-memory access time when all cores are used to execute the application threads.
Execution cycles on
N-core execution
↓ , ↑ ⇒ Benchmark programs are more beneficial
↓ , ↑ ⇒ Our approach is more effective
Execution time in clock cycles on an N-core CMP
Assumption: Execution threads is fixed in whole program execution The best numbers of helper-cores are given
Simulation Parameters: 8 in-order cores, 1MB L2 cache, 300 clock cycles Main Memory latency
Our approach improves performance by up to 47% (Cholesky).